## Slide 1: Cleaning Robot with Automatic Cleaning mechanism
TEAM B5 SRR. Sandeep cb.ai.u4aid2140 Siva Sai Kumar cb.ai.u4aid23156 D,Mahadev Naidu cb.ai.u4aid23111 K.Manoj Kumar cb.ai.u4aid23161
Mobile Robotics IOT

## Slide 2
INTRODUCTION
The development of autonomous cleaning solutions represents a significant advancement in both domestic and industrial maintenance technologies. Our team has designed and implemented an intelligent cleaning robot that combines navigation capabilities with specific chemical detection and targeted sanitization.
This project addresses the growing need for automated cleaning systems that can not only navigate spaces efficiently but also identify and respond to specific contaminants—particularly alcohol-based substances that are common in many environments.
The integration of sensing technologies, mechanical systems, and decision-making algorithms in our robot demonstrates the practical application of robotics principles to solve real-world cleaning challenges.

## Slide 3
S. No | Title | Year | Contribution | Drawbacks
1 | Automatic Floor Cleaner by Manya Jain, Pankaj Singh Rawat, Assist. Prof. Jyoti Morbale | 2019 | •Proposes a cost-effective and efficient automatic floor cleaning robot. •Focuses on simple design and functionality for household use. •Uses basic sensors and microcontrollers for obstacle avoidance and navigation. | •Limited advanced features like IoT integration or advanced path planning. •May not handle complex environments or multiple floor types effectively. •Lack of detailed performance metrics or scalability analysis.
2 | Design and Development of Floor Cleaner Robot (Automatic and Manual) by Manreet Kaur, Preeti Abrol | 2021 | •Presents a dual-mode robot (automatic and manual) for flexibility in operation. •Focuses on user-friendly design and affordability. •Includes basic navigation and cleaning mechanisms. | •Limited discussion on advanced navigation algorithms or IoT integration. •Manual mode dependency reduces full autonomy. •No detailed analysis of cleaning efficiency or power consumption.
3 | Path Planning and Guidance Techniques for an Autonomous Mobile Cleaning Robot by Christian Hofner, Gunther Schmidt | 2018 | •Provides a detailed analysis of path planning algorithms for autonomous robots. •Discusses guidance techniques for efficient coverage and obstacle avoidance. •Lays the groundwork for advanced navigation systems in cleaning robots. | •Focuses primarily on navigation and lacks detailed discussion on cleaning mechanisms or IoT integration. •May not address modern advancements in robotics or IoT. •Limited practical implementation details or case studies.
4 | Designing and Optimization of an Autonomous Vacuum Floor Cleaning Robot | 2020 | •Focuses on optimizing the design and performance of an autonomous vacuum cleaning robot. •Discusses power efficiency, cleaning mechanisms, and navigation systems. •Provides insights into improving battery life and cleaning effectiveness. | •Limited discussion on IoT integration or remote monitoring capabilities. •May not address multi-surface cleaning or advanced path planning algorithms. •Lack of detailed experimental validation or real-world testing data.
LITERATURE REVIEW

## Slide 4
Primary Objective: Design and develop a fully autonomous robot capable of detecting and cleaning alcohol-based substances while navigating its environment.
Specific Goals:
  Implement reliable obstacle detection and avoidance using ultrasonic sensing
  Integrate accurate chemical recognition capabilities via gas sensor technology
  Develop an effective cleaning mechanism with a servo-controlled brush system
  Create a smart dispensing system that activates in response to detected substances
  Ensure energy-efficient operation with appropriate power management
  Develop robust control software that coordinates all robot functions
OBJECTIVE

## Slide 5
COMPONENTS
Microcontroller and Processing
Arduino Mega 2560
Motion Control System
L293D Motor Driver IC
DC Motors (×4)
Sensing and Detection
HC-SR04 Ultrasonic Sensor
MQ-3 Gas Sensor
Cleaning Mechanism
SG90 Servo Motor
Brush Assembly
Solution Dispensing System
  DC water pump (6V)
  Flow rate: 100ml/minute at max speed
  Silicone tubing (2mm inner diameter)
  100ml detergent cleaning solution
  Controlled via Arduino Mega and a relay module

## Slide 6
Structural Components
Chassis
  Material: Laser-cut acrylic (5mm thickness)
  Dimensions: 20cm × 15cm × 10cm
  Two-tier design for component separation
  Mounting points for all electronic and mechanical components
Four-Wheel Drive System with Differential Steering
  All-Wheel Drive Configuration:
    Four motorized wheels (each wheel powered by a DC motor)
    Diameter: 65mm
    Width: 26mm
    Rubber tread for improved traction
    Direct connection to DC motors via shaft couplers
  Motors controlled in pairs (left side/right side) via L293D driver
  Enhanced traction and stability on various surfaces
  Differential steering achieved through varying motor speeds on each side
  Superior maneuverability compared to two-wheel drive systems
  Improved climbing ability for traversing small obstacles or thresholds

## Slide 7
METHODOLOGY
Development Process
Planning and Design Phase
  Requirements analysis and specification
  Component selection based on functional requirements
  System architecture design and block diagram creation
  Mechanical layout planning and modeling
  Electrical schematic design
Hardware Implementation Phase
  Chassis fabrication from acrylic sheets
  Motor and wheel assembly mounting
  Electronic component installation and wiring
  Sensor placement optimization for maximum coverage
  Cleaning mechanism assembly and integration
  Power system implementation with voltage regulation
Software Development Phase
  Individual component testing and driver development
  Sensor calibration and testing procedures
  Algorithm development for core functionality
  Integration of subsystem code modules
  Implementation of main control loop

## Slide 8
SOFTWARE ALGORITHM DESIGN
Obstacle Avoidance Algorithm
Uses ultrasonic time-of-flight measurements to calculate distance (15cm)
Implements a threshold-based decision system(placed at 115 degrees initially)
When obstacle detected within threshold, robot executes turn maneuver
Simple but effective for controlled environments
Future enhancement: Proportional turning based on obstacle proximity
Chemical Detection Algorithm
MQ-3 sensor provides analog readings proportional to alcohol concentration
System uses calibrated threshold value to trigger cleaning response(resistance decreases and heat of MO increases to detect alcohol)
Readings filtered with running average to reduce false positives
Works effectively for common alcohol-based cleaning fluids and sanitizers
Cleaning Sequence Algorithm
Coordinated sequence of:
  Robot stopping
  Brush deployment via servo
  Solution dispensing via pump
  Brush agitation through servo oscillation
  System reset to continue navigation
Movement Control
Differential drive system with independent motor control
PWM-based speed control for consistent movement
Simple directional commands (forward, turn, stop)
Fixed-duration turning for predictable navigation

## Slide 9
Cleaning Mechanism demonstration:
https://youtu.be/TBVAAZOVQk8?si=CRH0QL2dpW1-bMZh

## Slide 10
Team Contributions
Siva Sai Kumar cb.ai.u4aid23156: Hardware integration, motor control
D.Mahadev Naidu cb.ai.u4aid23111: Sensor programming, obstacle avoidance
SRR. Sandeep cb.ai.u4aid2140 Chemical detection, cleaning mechanism
K.Manoj Kumar cb.ai.u4aid23161: System integration of obstacle avoidance and chemical detection, testing

## Slide 11
Project Achievements
Our cleaning robot successfully demonstrates the integration of multiple robotic subsystems into a cohesive, functional unit capable of:
Autonomous navigation with reliable obstacle avoidance
Specific chemical detection focusing on alcohol-based substances
Automated cleaning response with targeted solution deployment
Physical scrubbing action for effective contaminant removal
CONCLUSION